Roof Drain Marker Co., Inc.

Section 07 01 50 ROOF DRAIN MAINTENANCE MARKERS 
Guide Specification

This guide specification specifies Roof Drain Marker Co.'s patented roof drain maintenance marker. Roof Drain Marker Co. brings awareness to the value of flat roof drain maintenance, and enables safer quality inspections by making drain locations visible year-round. Our reversible roof drain flag markers make inspections of flat roof drains safer, faster, and more efficient.  Investing in roof drain flag markers along with regular roof housekeeping extends the life of your roof, increases its sustainability, and reduces the likelihood of costly spring time repairs.

Reversibility is a key Roof Drain Marker characteristic. Our users tag problem drains, or indicated serviced drains, by turning the marker over, so that the contrasting color is visible across the roof.

Specifier: Select section number and title from the options listed, based upon regional practice and the nature of the construction contract. The section can be used as a free-standing document, or essential content can be copied and pasted into one of several related roofing and roof drain specification sections to specify this accessory item.

This section is readily edited utilizing several common commercial specification software tools.

We recommend you consult with Roof Drain Marker Co., LLC., West Bridgewater, MA; (877) 571-6644; email: lmay@roofdrainmarker.com; www.roofdrainmarker.com.

Edit section number and title below based upon preference for locating section.

This document is Copyright© 2015 by Roof Drain Marker Co., LLC.

SECTION 07 01 50 – ROOF DRAIN MAINTENANCE MARKERS

SECTION 07 72 00 – ROOF DRAIN MAINTENANCE MARKERS

SECTION 22 14 26 – ROOF DRAIN MAINTENANCE MARKERS

GENERAL

SUMMARY

Section Includes:

Roof drain maintenance marker flags.

RELATED REQUIREMENTS

Section 22 14 26 "Roof Drains" for low-slope roof drains.

REFERENCES

ASTM International (ASTM): www.astm.org:

ASTM B 209 (ASTM B 209M) - Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate

ASTM B 221 (ASTM B 221M) - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes

ASTM D 256 - Standard Test Methods for Determining the Izod Pendulum Impact Resistance of Plastics

ASTM D 790 - Standard Test Methods for Flexural Properties of Unreinforced and Reinforced Plastics and Electrical Insulating Materials

ASTM F 593 - Standard Specification for Stainless Steel Bolts, Hex Cap Screws, and Studs

ACTION SUBMITTALS

Product Data: For roof drain markers, including:

Standard drawings illustrating product dimensions.

Installation instructions and recommendations.

Samples for Verification: For each product specified.

PRODUCTS

MANUFACTURERS

Basis-of-Design Product: Provide roof drain markers manufactured by Roof Drain Marker Co., LLC., West Bridgewater, MA; (877) 571-6644; email: lmay@roofdrainmarker.com; www.roofdrainmarker.com.

ROOF DRAIN MARKER

Specifier Note: In addition to the very durable mechanical connection to the roof drain dome, a distinguishing characteristic of the Roof Drain Marker is its easy reversibility. This allows maintenance personnel to tag drains to indicate their status.

Roof Drain Marker: Drain dome-mounted vertical fiberglass flag marker secured in aluminum socket in turn secured with pre-punched aluminum bracket configured for secure through-bolting centered over roof drain dome.

Flag Marker: Pultruded fiber-reinforced polymer rod, 1/2 inch (12 mm) diameter by 48 inch (1219 mm) long, with reflective dual-colored reversible ends enabling marking of selected drains.

Flexural Strength, minimum, ASTM D 790, 700,000 psi (689 MPa).

Impact Strength, minimum, ASTM D 256: 40 ft-lb/in.

Marker Base: 1 by 1 by 4 inch (25 by 25 by 102 mm) extruded aluminum bar, ASTM B 209 (ASTM B 209M), with milled flag receiver, threaded flag set screw retainer, and threaded base.

Flag Bracket: 1 by 11 by 0.063 inch (25 by 25 by 1.60 mm) aluminum plate bracket, ASTM B 221 (ASTM B 221M).

Fasteners: Alloy Group 2 (A4) stainless-steel bolts, ASTM F 593 (ASTM F 738M), and nuts, ASTM F 594 (ASTM F 836M).

EXECUTION

EXAMINATION

Examine roof drain dome conditions to verify adequate attachment to drain base and compatible alignment with roof drain marker mounting bracket.

ROOF DRAIN MARKER INSTALLATION

Install roof drain markers on each roof drain dome in roof area indicated. Install in accordance with manufacturer's instructions.

Attach bracket to drain dome using manufacturer-furnished corrosion-resistant fasteners, securely tightened.

Thread marker base to threaded stud on marker bracket and tighten securely.

Insert flag marker into marker base and secure using set screw. Coordinate selection of colored flag marker end based upon drain condition.

END OF SECTION